## Slide 1: Revision and Preparation and Guideline for Assessment 3
Week 12
Dr. Farshid Keivanian

## Slide 2: Assessment 3: From Network Design to Troubleshooting
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Apply networking knowledge to realistic workplace problems.
Diagnose and correct faults in an existing network.
Design and configure a network for two departments.
Test connectivity, security and remote access.
Explain your work through a technical report, presentation and viva.

## Slide 3: Assessment 3: From Network Design to Troubleshooting
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Australian example: A junior network engineer working for a Sydney IT services company may be asked to investigate a network outage and set up connectivity for a new office.
Discussion: Why is a working Packet Tracer network not enough on its own?
Answer: A network engineer must also explain the design, prove that it works and document how problems were resolved.

## Slide 4: Assessment Structure and Marking
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Assessment component | Marks
Scenario 1 – Troubleshooting and diagnosis | 16
Scenario 2 – Network architecture and IPv4 design | 10
Scenario 2 – Configuration, security and testing | 12
Technical analysis and design justification | 5
Technical report, presentation and viva | 7
Total | 50

## Slide 5: Assessment Structure and Marking
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The rubric assesses both practical implementation and technical understanding.
Students should review all five criteria before beginning.
Evidence should correspond to the actual submitted Packet Tracer files.
Discussion: Can a student achieve the highest marks by submitting only screenshots of a working network?
Answer: No. The rubric also requires accurate explanations, diagnostic reasoning, design justification, professional documentation and viva performance.

## Slide 6: What Skills Will You Develop?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Network design: choosing devices and planning connections.
IP addressing: configuring subnets and default gateways.
Cisco IOS: configuring and checking routers and switches.
Troubleshooting: identifying faults and testing solutions.
Network security: protecting devices and configuring remote access.
Technical communication: reporting and explaining your decisions.

## Slide 7: What Skills Will You Develop?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Australian example: These skills are useful in IT support teams, managed service providers, universities and corporate networks across Australia.
Discussion: Which skill is most important when a user reports that the network has stopped working?
Answer: Troubleshooting, supported by knowledge of addressing, routing, devices and network protocols.

## Slide 8: Career Opportunities in Australia
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Job title | Relevant assessment skills
IT Support Officer | Connectivity testing and fault diagnosis
Service Desk Analyst | Troubleshooting and technical communication
Network Support Technician | Switches, routers and IP configuration
Junior Network Administrator | Network maintenance and documentation
Network Operations Centre (NOC) Analyst | Monitoring and incident investigation
Junior Network Engineer | Network design, routing and security
Students can explore entry-level and developing career opportunities such as:

## Slide 9: Career Opportunities in Australia
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Search on SEEK Australia or LinkedIn Jobs using terms such as Junior Network Engineer, Network Support, NOC Analyst and Cisco Networking.
Discussion: Which job would benefit most from knowing how to use show ip route?
Answer: Network support, network administration and NOC roles, because they frequently investigate routing and connectivity problems.

## Slide 10: Understand the Two Assessment Scenarios
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Scenario 1 – Troubleshooting
Investigate an existing Packet Tracer network.
Complete four troubleshooting/information-gathering tickets.
Use permitted Cisco IOS commands.
Identify faults and provide corrective commands where applicable.
Answer route and round-trip-time questions.

## Slide 11: Understand the Two Assessment Scenarios
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Scenario 2 – Network design
Redesign the ABC company network.
Connect HR and Finance through a shared ISP connection.
Plan for future devices.
Configure and verify the required network services.
Provide technical evidence and design justification.

## Slide 12: Understand the Two Assessment Scenarios
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: What is the main difference between the scenarios?
Answer: Scenario 1 focuses on diagnosing an existing network; Scenario 2 focuses on designing and implementing a network to meet business requirements.

## Slide 13: Read the Network Topology Before Configuring
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Identify:
Routers and switches.
PCs, servers and other end devices.
LAN and WAN connections.
Interface names and IP addresses.
Default gateways and routing paths.
Existing connections and possible points of failure.

## Slide 14: Read the Network Topology Before Configuring
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Australian example: Before changing a network in a Melbourne office, a technician reviews the network diagram to avoid disconnecting the wrong department.
Discussion: Why should you inspect the topology before entering Cisco commands?
Answer: To understand how devices connect and avoid making changes to the wrong interface or device.

## Slide 15: Read the Network Topology Before Configuring
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
This diagram shows how routers, switches and computers are connected in Scenario 1. The red lines represent serial connections between routers, while the black lines show Ethernet connections.

## Slide 16: Essential IPv4 Addressing Knowledge
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
An IPv4 address identifies a network interface.
A subnet mask identifies the network and host portions.
Devices in the same subnet can normally communicate directly through a switch.
Devices in different subnets need routing.
A default gateway is used to reach destinations outside the local subnet.

## Slide 17: Essential IPv4 Addressing Knowledge
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Device | IP address | Mask | Gateway
PC-A | 192.168.1.10 | 255.255.255.0 | 192.168.1.1
PC-B | 192.168.2.10 | 255.255.255.0 | 192.168.2.1
Example
Discussion: Can these two PCs communicate through switches alone?
Answer: Not under normal Layer 2 switching. A router or Layer 3 switch is needed between their different IP subnets.

## Slide 18: Subnetting and Future Network Growth
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Calculate how many IP-enabled devices each department requires.
Include network infrastructure interfaces and future expansion.
Select a suitable subnet size.
Avoid overlapping subnet ranges.
Document the addressing scheme.

## Slide 19: Subnetting and Future Network Growth
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Department | Current end devices | Example subnet
HR | 12 | 192.168.10.0/27
Finance | 16 | 192.168.20.0/27
Illustrative planning example
Both /27 networks provide 30 usable IPv4 addresses. These are teaching examples, not prescribed assessment addresses.
Discussion: Why might a /28 subnet be unsuitable for Finance?
Answer: It provides only 14 usable addresses, which is fewer than Finance's 16 listed end devices, even before allowing for a gateway or future growth.

## Slide 20: Switches, Routers and Internet Connectivity
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Switches connect devices within a local network.
Routers connect different IP networks.
A default gateway forwards traffic outside the local subnet.
An ISP connection provides a route towards the Internet.
NAT/PAT may allow multiple private IPv4 devices to share a public IPv4 address.

## Slide 21: Switches, Routers and Internet Connectivity
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Australian example: A small Sydney business may connect its HR and Finance networks to one business Internet service.
Discussion: Does connecting a router to an ISP automatically give every PC Internet access?
Answer: No. Correct addressing, gateways, routing, ISP connectivity and often NAT and DNS are also required.

## Slide 22: Switches, Routers and Internet Connectivity
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
This diagram shows how the HR and Finance departments connect to the Internet through their network devices. Both departments can access the Internet while using separate local networks.

## Slide 23: Cisco IOS Command Modes
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Mode | Example prompt | Purpose
User EXEC | Router> | Basic monitoring
Privileged EXEC | Router# | Advanced monitoring
Global configuration | Router(config)# | Device-wide configuration
Interface configuration | Router(config-if)# | Interface settings

## Slide 24: Cisco IOS Command Modes
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Example commands:
enable
configure terminal
interface gigabitEthernet 0/0
exit
end
Discussion: Why does ip address not normally work at the Router# prompt?
Answer: Interface IP addresses are configured in interface configuration mode.

## Slide 25: Cisco IOS Command Modes
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Cisco routers have different command modes for viewing information and changing settings. To configure an IP address, we must enter interface configuration mode using commands such as configure terminal and interface g0/0.

## Slide 26: Scenario 1 – Troubleshooting and Diagnostic Reasoning
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Scenario 1: Understand the Existing Network
The supplied topology includes:
Routers R1, R2 and R3.
Switches SW0, SW1, SW2 and MGT-SW.
PC-A as the illustrated management PC.
Ethernet connections between network devices.
Serial connections between routers.
VLAN interfaces and router loopback interfaces.

## Slide 27: Scenario 1 – Troubleshooting and Diagnostic Reasoning
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The task sheet also identifies a correctly configured USER-PC at 5.5.5.101/24.
Discussion: Why should you avoid changing USER-PC settings?
Answer: The task states that USER-PC is already correctly configured. Troubleshooting should focus on the affected network devices.

## Slide 28: Scenario 1 – Troubleshooting and Diagnostic Reasoning
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
This diagram shows the existing network that students need to troubleshoot in Assessment 3. Students should examine the connections between devices and identify possible causes of communication problems.

## Slide 29: Troubleshooting: Identify, Test and Fix
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use a systematic process:
Read the reported problem.
Identify the affected source and destination.
Check the relevant interface status and addressing.
Examine routing or protocol information.
Identify the likely cause.
Apply a targeted correction.
Test again and record the result.

## Slide 30: Troubleshooting: Identify, Test and Fix
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why should you not immediately change several router settings when a ping fails?
Answer: Multiple changes make it difficult to identify the original cause and may introduce additional problems.

## Slide 31: Troubleshooting: Identify, Test and Fix
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Troubleshooting involves identifying the problem, checking network settings, testing possible causes and applying a solution. After fixing the problem, we must test the network again to confirm that it works.

## Slide 32: Checking Interface Status
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
show ip interface brief
show interfaces
Interpret common results:
up/up: interface and line protocol are operational.
administratively down/down: interface is disabled.
down/down: possible physical or connection problem.
up/down: interface is active but the line protocol is not operational.

## Slide 33: Checking Interface Status
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: What would you investigate if an interface is administratively down?
Answer: Whether it should be enabled using no shutdown, after confirming that it is the correct interface.

## Slide 34: Checking Interface Status
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The command show ip interface brief displays the IP addresses and status of router interfaces. An interface that is administratively down can be enabled using no shutdown, provided there are no other connection problems.

## Slide 35: Troubleshooting Switch VLAN Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
A switch virtual interface (SVI) can provide an IP address for switch management.
Useful commands:
show ip interface brief
show interface vlan 1
show vlan brief

## Slide 36: Troubleshooting Switch VLAN Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Check:
VLAN interface IP address and mask.
SVI operational status.
Whether the VLAN exists and has an active associated port.
Default gateway for management traffic outside the subnet.

## Slide 37: Troubleshooting Switch VLAN Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why might a switch management VLAN be unreachable even when its IP address is correct?
Answer: The SVI may be down, the VLAN may not have an active port, or the switch may lack the correct management default gateway.

## Slide 38: Understanding Routing Tables
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
show ip route
Common route codes:
C – directly connected network.
L – local interface address.
S – static route.
D – EIGRP-learned route, where supported and configured.
Check whether the destination network appears in the routing table.

## Slide 39: Understanding Routing Tables
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: A router can ping its directly connected network but cannot reach a remote loopback. What should you inspect?
Answer: Its routing table and the return route from the destination.

## Slide 40: Understanding EIGRP Neighbours
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The Scenario 1 appendix identifies EIGRP diagnostic commands.
Examples:
show ip eigrp neighbors
show ip eigrp traffic
show ip route

## Slide 41: Understanding EIGRP Neighbours
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
EIGRP can exchange routing information between configured neighbouring routers.
Possible problems include:
Incorrect interface addressing.
Inactive interfaces.
Incompatible EIGRP settings.
Missing network participation or filtering.

## Slide 42: Understanding EIGRP Neighbours
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why can two routers have an operational link but fail to exchange EIGRP routes?
Answer: Their routing protocol configurations may not allow them to form an EIGRP neighbour relationship.

## Slide 43: Understanding EIGRP Neighbours
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
EIGRP allows routers to exchange routing information and learn how to reach other networks. The commands show ip eigrp neighbors and show ip route eigrp help us check neighbouring routers and routes learned through EIGRP.

## Slide 44: Testing Connectivity with Ping
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
ping 192.168.1.1
Ping uses ICMP Echo Request and Echo Reply messages.
It helps test whether a destination responds and may report round-trip time.
A failed ping can have several causes, including incorrect addressing, missing routes, interface problems or traffic filtering.

## Slide 45: Testing Connectivity with Ping
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Does a failed ping always mean the destination device is switched off?
Answer: No. The problem may be elsewhere in the network, or ICMP (Internet Control Message Protocol) may be blocked.

## Slide 46: Testing Connectivity with Ping
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Question: You can open a website hosted on a server, but when you ping the server, you receive "Request timed out." Does this mean the server is offline?
Answer: No. The server may be working correctly, but its firewall could be blocking ICMP Echo Requests or Replies while allowing web traffic (HTTP/HTTPS).

## Slide 47: Finding the Route with Traceroute
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
On Cisco IOS:
traceroute 192.168.10.10
Traceroute helps identify Layer 3 hops along a path.
It can assist with:
Investigating unexpected routes.
Identifying where responses stop.
Comparing the observed route with the network design.

## Slide 48: Finding the Route with Traceroute
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Some hops may not respond, even when traffic can continue.
Discussion: Why does traceroute normally show routers rather than ordinary Layer 2 switches?
Answer: Routers decrement the IP TTL and can generate the responses used by traceroute. Ordinary Layer 2 switches do not act as IP routing hops.

## Slide 49: Measuring Round-Trip Time
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Round-trip time (RTT) is the time taken for a request to reach its destination and for the response to return.
Example ping results:
First reply: 4 ms.
Second reply: 6 ms.
Third reply: 5 ms.
Average RTT:

## Slide 50: Measuring Round-Trip Time
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Does a lower RTT always mean that a network has higher bandwidth?
Answer: No. RTT measures delay, while bandwidth describes data-carrying capacity.

## Slide 51: Reading Router Hardware and Software Information
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
show version
Depending on the device and IOS output, this may show:
Cisco IOS version.
Router model.
System image.
Memory information.
Configuration register.
Hardware information.

## Slide 52: Reading Router Hardware and Software Information
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The Scenario 1 task specifically asks students to identify the IOS version, NVRAM and ROM size for R2.
Discussion: Why should you report the values from R2 rather than another router?
Answer: Different devices may have different hardware, software and memory information.

## Slide 53: Reading Router Hardware and Software Information
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The command show version displays important information about a Cisco router, including its IOS version, hardware and memory. Network administrators use this information when checking device specifications or troubleshooting software problems.

## Slide 54: Scenario 2: ABC Company Requirements
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Requirement | HR | Finance
PCs | 10 | 12
IP phones | 1 | 2
Wireless printers | 1 | 1
Scanners | 0 | 1
Current end devices | 12 | 16
ABC Company has two departments.

## Slide 55: Scenario 2: ABC Company Requirements
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Both departments require:
Internet connectivity through a shared ISP connection.
Capacity for future expansion.
Reliable communication.
Finance specifically requires secure and reliable systems.
Discussion: Why should Finance receive particular attention during network design?
Answer: It handles business information that may be sensitive and requires appropriate access controls, reliability and protection.

## Slide 56: Designing a Suitable Network Topology
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
A suitable design should consider:
Separate logical networks for HR and Finance.
Enough wired and wireless connectivity.
A router or Layer 3 device for inter-network communication.
A shared path towards the ISP.
Additional ports and address capacity for future growth.
Appropriate access controls between departments.

## Slide 57: Designing a Suitable Network Topology
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why might separate VLANs be useful for HR and Finance?
Answer: VLANs create separate Layer 2 broadcast domains and can support more organised and controlled network access when combined with appropriate routing and security policies.

## Slide 58: Designing a Suitable Network Topology
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
This diagram shows a possible network design for ABC Company, with separate HR and Finance networks. Both departments connect through a shared router to access the Internet using one ISP connection.

## Slide 59: Configuring Router Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Illustrative Cisco IOS configuration:
enable
configure terminal
interface gigabitEthernet 0/0
description HR LAN
ip address 192.168.10.1 255.255.255.224
no shutdown
exit
Check using:
show ip interface brief

## Slide 60: Configuring Router Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: What happens if the router interface and HR computers use different, non-overlapping IP subnets?
Answer: The computers will not be able to use that interface as a directly reachable default gateway without correcting the addressing.

## Slide 61: Configuring Router Interfaces
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Router interfaces need correct IP addresses and must be enabled before they can communicate. After configuring an interface, use show ip interface brief to check whether its status is up/up.

## Slide 62: Configuring End Devices and Default Gateways
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Each end device needs appropriate settings:
IP address.
Subnet mask.
Default gateway.
DNS server, where name resolution is required.

## Slide 63: Configuring End Devices and Default Gateways
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Example HR PC:
IP address: 192.168.10.10
Subnet mask: 255.255.255.224
Default gateway: 192.168.10.1
Discussion: A PC can ping another PC in the same subnet but cannot reach Finance. What should you check first?
Answer: The PC's default gateway and the routing between the two departmental networks.

## Slide 64: Remote Access: SSH and Telnet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Telnet provides remote command-line access but does not encrypt the session.
SSH encrypts remote management traffic.
SSH is preferred for secure administration.
Router and switch remote access should be restricted to authorised users.

## Slide 65: Remote Access: SSH and Telnet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Illustrative SSH configuration:
hostname HR-Router
ip domain-name abc.example
username admin privilege 15 secret ExampleOnly123!
crypto key generate rsa
ip ssh version 2
line vty 0 4
login local
transport input ssh

## Slide 66: Remote Access: SSH and Telnet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The example credentials are for classroom practice only and must not be reused as real passwords. RSA key generation may require a key-size selection, depending on IOS.
Discussion: Why is SSH generally safer than Telnet?
Answer: SSH encrypts the management session, reducing the risk of exposing credentials and commands.

## Slide 67: Remote Access: SSH and Telnet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
SSH allows an authorised network administrator to connect securely to a router from another computer. Unlike Telnet, SSH encrypts the communication, helping protect usernames, passwords and commands.

## Slide 68: Connecting Both Departments to the Internet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
A shared ISP connection requires an end-to-end design.
Consider:
Correct department IP addressing.
Appropriate routing between networks.
A default route towards the ISP.
NAT/PAT where private IPv4 addresses are used.
DNS and any required ISP-side settings.
Appropriate security rules.

## Slide 69: Connecting Both Departments to the Internet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why might two private departmental networks need NAT/PAT to access the public Internet?
Answer: Private IPv4 addresses are not globally routed on the public Internet. NAT/PAT can translate internal addresses to a suitable public address.

## Slide 70: Connecting Both Departments to the Internet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
NAT/PAT allows multiple computers with private IP addresses to access the Internet through a shared public IP address. In this example, both HR and Finance can use the same Internet connection without requiring a separate public IP address for every computer.

## Slide 71: Network Testing and Evidence
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Test the network systematically:
Check interface status.
Verify device IP addresses.
Ping the local default gateway.
Test communication between authorised departments.
Test access towards the simulated ISP.
Test SSH remote access.
Verify routes and save configurations.

## Slide 72: Network Testing and Evidence
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Useful commands:
show ip interface brief
show ip route
ping <destination-IP>
traceroute <destination-IP>
show running-config
copy running-config startup-config

## Slide 73: Network Testing and Evidence
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why should screenshots show actual command results rather than just the topology?
Answer: A topology shows the intended connections, while command outputs provide evidence that the configuration and tests were performed.

## Slide 74: What to Do and What to Avoid
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
What to do
Read both scenarios carefully.
Keep a record of original faults.
Test one correction at a time.
Use accurate subnet masks and gateways.
Configure the required security controls.
Save configurations and Packet Tracer files.
Provide genuine screenshots and command evidence.
Explain your design decisions.

## Slide 75: What to Do and What to Avoid
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
What to avoid
Guessing fault causes without evidence.
Changing unrelated configurations.
Reusing a previous ticket's solution.
Assigning overlapping IP subnets.
Assuming an ISP connection works without testing.
Using Telnet as the preferred secure management method.
Submitting screenshots that do not match the final files.
Copying another student's work.

## Slide 76: What to Do and What to Avoid
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: Why should you save a copy of the original troubleshooting file?
Answer: It allows you to compare the original and corrected network and recover if an incorrect change causes additional problems.

## Slide 77: Submission Checklist
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Completed all four Scenario 1 tickets
Answered the route and RTT questions
Recorded diagnostic commands, findings and corrective commands
Completed the Scenario 2 network design
Included the required HR and Finance devices
Checked subnet masks, IP addresses and gateways
Configured and tested the required routing and remote-access services

## Slide 78: Submission Checklist
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Renamed one router with my first name, one with my last name and one switch with my student ID
Saved and reopened both Packet Tracer files
Prepared the technical report with screenshots and command evidence
Explained design decisions, security, scalability and sustainability
Prepared the required seven-minute presentation with face overlay
Checked the online viva arrangements
Reviewed the Canvas rubric and submission deadline

## Slide 79: Submission Checklist
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Submission reminder: Based on the A3 guide, the required artefacts include the two .pkt files, technical report PDF, configuration evidence and presentation.

## Slide 80: Final Revision: Think Like a Network Engineer
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Before your viva, be ready to answer:
What problem did you identify?
Which command helped you find it?
Why did you select that command?
What did you change?
How did you verify the correction?
Why did you select your network design?
How did you improve security and scalability?
What would you do differently in a real workplace?

## Slide 81: Final Revision: Think Like a Network Engineer
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion: What is the difference between memorising Cisco commands and understanding networking?
Answer: Memorising helps you recall commands. Understanding helps you select the right command, interpret the result, identify the problem and explain the solution.

## Slide 82: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Students must submit the following:
Scenario 1 – Completed Cisco Packet Tracer .pkt file.
Scenario 2 – Completed Cisco Packet Tracer .pkt file.
Technical Design and Troubleshooting Report in PDF format.
Seven-minute recorded presentation with face overlay, or attend the scheduled live presentation as instructed.
Attend the compulsory online viva at the allocated time.

## Slide 83: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Important reminders:
Submit files individually through Canvas.
Do not submit ZIP or RAR files unless specifically instructed.
Ensure both Packet Tracer files open correctly.
Check that the report and presentation match the final configurations.

## Slide 84: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Can students submit only the PDF report and screenshots without their Packet Tracer files?
Answer: No. Both completed .pkt files are compulsory.

## Slide 85: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
How to Prepare Your Technical Report
Recommended report structure:
Student details and assessment overview.
Scenario 1 – Troubleshooting tickets, identified problems, diagnostic commands and corrections.
Scenario 1 – Route identification and RTT calculations.
Scenario 2 – Proposed network topology and addressing plan.
Scenario 2 – Device configurations, security and remote access.
Connectivity testing, screenshots and command outputs.
Technical explanations, design justification, scalability and sustainability.
Conclusion, references where applicable, and AI-use statement.

## Slide 86: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Important: Screenshots should be readable, clearly labelled and consistent with the submitted Packet Tracer files.
Discussion question: Why should the report include both diagnostic commands and their outputs?
Answer: The commands explain how the network was investigated, while the outputs provide evidence supporting the findings.

## Slide 87: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Section | Time
Introduction and assessment objectives | 30 seconds
Scenario 1 – Troubleshooting approach and results | 2 minutes
Scenario 2 – Network design and addressing | 1.5 minutes
Configuration, security and connectivity testing | 2 minutes
Conclusion and key learning outcomes | 1 minute
Total | 7 minutes
Preparing Your Seven-Minute Presentation
Suggested presentation structure:

## Slide 88: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Presentation requirements:
Explain the work in your own words.
Show the relevant Packet Tracer topology and evidence.
Explain important decisions rather than reading every configuration command.
Use a clear voice and professional language.
Include the required face overlay for a recorded presentation.

## Slide 89: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Should students spend most of their presentation reading Cisco commands?
Answer: No. They should focus on what they implemented, why they selected that approach and how they verified that it worked.

## Slide 90: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Academic Integrity and Responsible AI Use
Permitted AI support, subject to Canvas instructions:
Understanding networking concepts.
Brainstorming high-level design considerations.
Improving grammar and report clarity.
Identifying areas where explanations need improvement.

## Slide 91: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Not permitted:
Using AI to generate the final network design.
Using AI to complete troubleshooting tickets.
Submitting AI-generated configuration commands as your own work.
Generating substantial report or presentation content.
Fabricating screenshots, command outputs or testing results.
Students must include a brief AI-use statement in the report, including any additional disclosure required by the assessment instructions.

## Slide 92: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Can a student use AI to generate all the configuration commands and submit them without understanding them?
Answer: No. The guide prohibits AI-generated configuration commands for submission. Students must complete their own technical work and explain it during the viva.

## Slide 93: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Final Preparation for the Online Viva
During the compulsory viva, students may be asked to:
Open their submitted Packet Tracer files.
Explain how they identified a network fault.
Demonstrate a relevant Cisco IOS command.
Explain why a particular subnet or gateway was selected.
Justify security and remote-access configurations.
Interpret ping, traceroute or routing results.
Explain how their network supports future growth.
Demonstrate that they understand their own report and presentation.

## Slide 94: Additional Notes about Assessment 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: What should you do if the lecturer asks why you selected a particular network configuration?
Answer: Explain the technical reason, relate it to the network requirements and show relevant evidence from your submitted work.

## Slide 95: Let’s Answer Your Questions
Canvas Inbox – For academic queries.
Email – For formal communication and attachments.
Canvas Discussion – For academic discussions and general queries.
Reminder – Please follow up if you do not receive a response within 3 business days.

## Slide 96
Happy Learning and Bright Futures Ahead! Dr. Farshid Keivanian Stay Connected: linkedin.com/in/farshid-keivanian github.com/FarshidKeivanian
Education is the most powerful weapon you can use to change the world. — Nelson Mandela