## Slide 1: Subnetting Practice Week
Week 8
Dr. Farshid Keivanian

## Slide 2: Today we practise IPv4 subnetting.
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
By the end of this class, you should be able to:
identify the subnet mask and prefix
calculate network and broadcast addresses
find first and last usable host addresses
calculate the number of usable hosts
calculate the number of created subnets
solve AT2-style subnetting problems

## Slide 3: Today we practise IPv4 subnetting.
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Key idea:
This week is mainly about solving problems, not learning many new concepts.
Australian example: Imagine you are designing IP networks for different departments in an Australian university campus.

## Slide 4: Why Are We Practising Subnetting?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Subnetting is used to divide one large IP network into smaller networks.
This helps us:
organise devices
reduce unnecessary broadcast traffic
use IP addresses efficiently
separate departments or locations
design scalable networks

## Slide 5: Why Are We Practising Subnetting?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Australian example:
An Australian university might use separate subnets for:
Student Labs
Staff Offices
Library
Wi-Fi
Security Cameras

## Slide 6: Why Are We Practising Subnetting?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Why not place every device in one very large network?
Because a large network creates more broadcast traffic and is harder to manage.

## Slide 7: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
AT2 – VLSM Subnetting
Assessment Task 2 requires you to apply IPv4 subnetting and Variable Length Subnet Masking (VLSM) skills to a realistic network scenario.
For each network segment, you may need to determine:
the required number of usable hosts;
the appropriate prefix length (for example, /23, /24 or /26);

## Slide 8: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
the subnet mask;
the network address;
the first usable host address;
the last usable host address;
the broadcast address; and
an efficient allocation of the available IP address space.

## Slide 9: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Important:
You need to show your calculations.
Do not only write the final answer.
Discussion question: Why should you show your working in AT2?
Because the calculation demonstrates that you understand how the answer was obtained.

## Slide 10: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
When using VLSM, remember to allocate the networks from the largest host requirement to the smallest and make sure that the allocated subnets do not overlap and remain within the given address block.

## Slide 11: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Important) Show your calculations and working clearly.
Do not simply write the final addresses in the table. Your working should demonstrate how you determined the appropriate subnet size, prefix length and address range.
Discussion Question) Why is it important to show your working in AT2?

## Slide 12: Connection to Assessment Task 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Because the calculations demonstrate that you understand how the subnet size and address range were determined, rather than simply providing a final answer. Clear working also makes it possible to check your subnetting process and identify any mistakes.

## Slide 13: What Information Can We Find?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 14: What Information Can We Find?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 15: What Information Can We Find?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 16: What Information Can We Find?
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 17: Four Questions to Think About
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Try these before we continue.
Question 1
A network uses /28.
How many usable hosts can it support?
Answer: 14

## Slide 18: Four Questions to Think About
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Question 2
How many bits must be borrowed to create at least 5 subnets?
2² = 4 not enough
2³ = 8 enough
Answer: 3 bits

## Slide 19: Four Questions to Think About
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Question 3
How many usable hosts are available with:
255.255.255.248
This is /29.
Host bits = 3
2³ - 2 = 6
Answer: 6 usable hosts

## Slide 20: Four Questions to Think About
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Question 4
What prefix is:
255.255.255.224
Answer: /27

## Slide 21: IPv4 Addresses Have 32 Bits
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
An IPv4 address contains: 32 bits
It is divided into four groups.
Each group contains: 8 bits
Each group is called an octet.
Example: 192.168.10.25 has four octets:
192 | 168 | 10 | 25
Discussion question: How many bits are in one IPv4 octet?
Answer: 8 bits.

## Slide 22: Binary Values Inside One Octet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Remember the binary positions:
128 64 32 16 8 4 2 1
If the bit is 1, include the value.
If the bit is 0, ignore the value.
Example: 11000000
means:
128 + 64 = 192
Therefore:
11000000 = 192

## Slide 23: Quick Binary Practice
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Convert: 11100000
Use:
128 + 64 + 32
Result:
224
Discussion question: What is 11110000 in decimal?
Answer:
128 + 64 + 32 + 16 = 240

## Slide 24: Important Subnet Mask Values
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Binary | Decimal
00000000 | 0
10000000 | 128
11000000 | 192
11100000 | 224
11110000 | 240
11111000 | 248
11111100 | 252
11111110 | 254
11111111 | 255
Memorise this pattern:
These values appear frequently in subnetting.

## Slide 25: Prefix Length Review
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
The prefix tells us how many bits belong to the network.
Example:
/24
means:
24 network bits
8 host bits
because:
32 - 24 = 8

## Slide 26: Prefix and Mask Examples
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
/24 = 255.255.255.0
/25 = 255.255.255.128
/26 = 255.255.255.192
/27 = 255.255.255.224
/28 = 255.255.255.240
/29 = 255.255.255.248
/30 = 255.255.255.252
Discussion question) What is the subnet mask for /27?
Answer) 255.255.255.224

## Slide 27: Network Bits vs Host Bits
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Every IPv4 address contains two logical parts:
Network portion | Host portion
The subnet mask tells us where the division occurs.
Example:
192.168.10.25/24
can be viewed as:
Network: 192.168.10
Host: 25

## Slide 28: Australian Example: University Lab
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Suppose ACU has: 192.168.40.0/24
for a computer laboratory.
Possible devices:
192.168.40.10
192.168.40.20
192.168.40.50
All belong to the same /24 network.

## Slide 29: Australian Example: University Lab
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Would 192.168.41.20/24 be in the same subnet?
No. Its network would be 192.168.41.0/24.

## Slide 30: The Two Special Addresses
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
In a traditional IPv4 subnet, two addresses are normally not assigned to hosts.
Network address
The first address.
Example: 192.168.10.0
Broadcast address
The last address.
Example: 192.168.10.255
for /24.

## Slide 31: Usable Host Range
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
For: 192.168.10.0/24
we have:
Network: 192.168.10.0
First host: 192.168.10.1
Last host: 192.168.10.254
Broadcast: 192.168.10.255
Discussion question) Can we assign 192.168.10.255 to a PC?
Answer: No. It is the broadcast address.

## Slide 32: Host Calculations
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
2^h - 2
where:
h = number of host bits
We subtract 2 for:
Network address
Broadcast address

## Slide 33: Example: /28
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
For /28:
32 - 28 = 4 host bits
Possible addresses:
2⁴ = 16
Usable hosts:
16 - 2 = 14
Therefore:
/28 → 14 usable hosts

## Slide 34: Practice: /27
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
For /27:
Host bits = 32 - 27
= 5
2⁵ = 32 addresses
32 - 2 = 30 usable hosts
Answer:
/27 supports 30 usable hosts

## Slide 35
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 36: Discussion: Allowing for Growth
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
A company currently has 28 devices.
Would /27 always be a good design?
Not necessarily.
/27 supports 30 usable hosts.
That leaves only:
2 spare addresses
A network designer may choose a larger subnet if significant growth is expected.

## Slide 37: Discussion: Allowing for Growth
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Discussion question: Why might /26 be better?
Answer: It allows up to 62 usable hosts and provides room for growth.

## Slide 38: Subnet Size and Block Size
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
What Is Block Size?
Block size tells us where each subnet begins.
A useful shortcut is: Block size = 256 - interesting mask value
Example:
/27
Mask: 255.255.255.224
Therefore: 256 - 224 = 32
Subnets increase by 32.

## Slide 39: /27 Subnet Boundaries
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Block size: 32
Therefore networks begin at:
0
32
64
96
128
160
192
224
So the /24 has been divided into 8 /27 subnets.

## Slide 40: Example /27
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
For: 192.168.1.75/27
Subnet ranges are:
0–31
32–63
64–95
96–127
...
75 falls inside:
64–95
Therefore:
Network: 192.168.1.64
Broadcast: 192.168.1.95

## Slide 41: Find the Host Range
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Continuing:
Network: 192.168.1.64
Broadcast: 192.168.1.95
First usable host:
192.168.1.65
Last usable host:
192.168.1.94

## Slide 42: Discussion Practice
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given: 192.168.1.170/27
Which range contains 170?
128–159
160–191
192–223
Answer: 160–191
Therefore:
Network: 192.168.1.160
Broadcast: 192.168.1.191
Hosts: 192.168.1.161–190

## Slide 43: Finding the Network Address Using AND
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Binary AND Operation
To calculate the network address exactly, computers use a binary AND operation.
Rules:
1 AND 1 = 1
1 AND 0 = 0
0 AND 1 = 0
0 AND 0 = 0

## Slide 44: Simple /24 Example
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
IP:
192.168.10.10
Mask:
255.255.255.0
AND result:
192.168.10.0
Therefore:
Network = 192.168.10.0

## Slide 45: Shortcut When Mask Contains 255 and 0
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
If a mask octet is: 255
the network result keeps the IP octet.
If the mask octet is: 0
the result becomes zero.
Example:
IP: 192.168.10.25
Mask: 255.255.255.0
Result: 192.168.10.0

## Slide 46: The Interesting Octet
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
You normally need detailed binary work only where the mask is neither: 255
nor: 0
Example:
IP: 172.30.239.145
Mask: 255.255.192.0
Only the third octet needs detailed calculation.

## Slide 47: Convert the Third Octet to Binary
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
IP third octet:
239
Binary:
11101111
Mask third octet:
192
Binary:
11000000

## Slide 48: Perform AND
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 49: Complete Network Address
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Therefore:
IP: 172.30.239.145
Mask: 255.255.192.0
Network: 172.30.192.0
Because:
172 stays
30 stays
239 AND 192 = 192
fourth octet becomes 0

## Slide 50: Australian Example: Enterprise Network
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 51: Discussion Question
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Why can't we identify the network from:
172.30.239.145
alone?
Answer:
Because we also need the subnet mask or prefix.
For example:
172.30.239.145/16
and:
172.30.239.145/18
belong to different subnet definitions.

## Slide 52: Host Bits and Number of Hosts
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
/18 Example
Mask:
255.255.192.0
Prefix:
/18
IPv4 has:
32 bits
Host bits:
32 - 18 = 14

## Slide 53: Hosts in a /18
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 54: Quick Prefix Table
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
/24 → 8 host bits → 254 usable
/25 → 7 host bits → 126 usable
/26 → 6 host bits → 62 usable
/27 → 5 host bits → 30 usable
/28 → 4 host bits → 14 usable
/29 → 3 host bits → 6 usable
/30 → 2 host bits → 2 usable
This is very useful for AT2.

## Slide 55: Class Challenge
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Which subnet is the smallest that supports 50 devices?
Try:
/27 → 30 usable
/26 → 62 usable
Answer:
/26

## Slide 56: Practice Set 1: Find Network and Broadcast
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
For each address:
Find the prefix
Find the block size
Identify the subnet containing the IP
Find network address
Find broadcast address
Find usable host range
Find usable hosts

## Slide 57: Practice 1
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given:
192.168.100.25/28
Before calculating, ask:
What is the block size?
Mask:
255.255.255.240
256 - 240 = 16

## Slide 58: Practice 1 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Subnets:
0–15
16–31
32–47
...
25 is inside:
16–31

## Slide 59: Practice 1 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Therefore:
Network: 192.168.100.16
First host: 192.168.100.17
Last host: 192.168.100.30
Broadcast: 192.168.100.31
Host bits: 4
Usable hosts: 14

## Slide 60: Practice 2
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 61: Practice 2 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Nearby ranges:
124–127
128–131
132–135
130 is inside:
128–131
Therefore:
Network: 172.30.10.128
First host: 172.30.10.129
Last host: 172.30.10.130
Broadcast: 172.30.10.131
Usable hosts: 2

## Slide 62: Australian Example: Point-to-Point Link
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 63: Practice 3
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given:
10.1.113.75/19
Mask:
255.255.224.0
Interesting octet:
third octet
Block size:
256 - 224 = 32

## Slide 64: Practice 3 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.

## Slide 65: Practice 4
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given:
198.133.219.250/24
Because /24 means:
255.255.255.0
Therefore:
Network: 198.133.219.0
Broadcast: 198.133.219.255
Host bits: 8
Usable hosts: 254

## Slide 66: Practice 5
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given: 128.107.14.191/22
Mask: 255.255.252.0
Block size in third octet: 256 - 252 = 4
Third-octet blocks:
0
4
8
12
16
...
14 belongs to:
12–15

## Slide 67: Practice 5 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Therefore:
Network: 128.107.12.0
Broadcast: 128.107.15.255
Host bits: 10
Usable hosts: 1022
Discussion question: What is the next subnet?
Answer:
128.107.16.0/22

## Slide 68: Practice 6
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Given: 172.16.104.99/27
Mask: 255.255.255.224
Block size: 32
Ranges:
64–95
96–127
128–159

## Slide 69: Practice 6 Solution
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
99 is inside:
96–127
Therefore:
Network: 172.16.104.96
First host: 172.16.104.97
Last host: 172.16.104.126
Broadcast: 172.16.104.127
Usable hosts: 30

## Slide 70: Creating Subnets by Borrowing Bits
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
What Does “Borrow Bits” Mean?
Suppose the original network is:
192.168.1.0/24
A /24 has:
8 host bits
If we change it to /27:
27 - 24 = 3 borrowed bits
These borrowed bits create additional subnets

## Slide 71: Number of Created Subnets
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Use:
2^s
where:
s = number of borrowed bits
Example:
3 borrowed bits
2³ = 8 subnets

## Slide 72: Example
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
Original: /24
New: /27
Borrowed bits: 27 - 24 = 3
Created subnets: 2³ = 8
Remaining host bits: 32 - 27 = 5
Usable hosts: 2⁵ - 2 = 30

## Slide 73: Class Question
3
Presentation_ID
© 2008 Cisco Systems, Inc. All rights reserved.
We start with: 192.168.10.0/24
We need at least 6 subnets.
How many bits should we borrow?
Try:
2² = 4
2³ = 8
Answer:
3 bits
New prefix: /27

## Slide 74: Let’s Answer Your Questions
Canvas Inbox – For academic queries.
Email – For formal communication and attachments.
Canvas Discussion – For academic discussions and general queries.
Reminder – Please follow up if you do not receive a response within 3 business days.

## Slide 75
Happy Learning and Bright Futures Ahead! Dr. Farshid Keivanian Stay Connected: linkedin.com/in/farshid-keivanian github.com/FarshidKeivanian
Education is the most powerful weapon you can use to change the world. — Nelson Mandela